## Slide 1: West Virginia Conservation Agency's Partnership with WVDEP to Delist Impaired Waterways
West Virginia Conservation Agency
Kara Grosso
Conservation Specialist
West Virginia Conservation Agency

## Slide 2: Impaired Waters and Department of Environmental Protection (DEP)
303(d) list of impaired and threatened waters
  State submits list to Environmental Protection Agency (EPA) every 2 years
  State identifies pollutant
Total Maximum Daily Loads (TMDL)
  Data and model driven
  Developed by DEP and approved by EPA
  Pollution source identification and plan of action
  Waterways tracked until fully restored
Common impairments in WV
  Fecal coliform
  Iron, aluminum, selenium
  pH

## Slide 3: Clean Water Act §319 Nonpoint Source (NPS) Pollution Program
WVDEP's NPS Program administers §319 grants
  Awarded by the USEPA Region III
  Projects that reduce NPS pollution
  Max grant reimbursement is 60% of the total project cost
  40% non-federal match requirement for each grant
Watershed Based Plan (WBP)
  Plan of action for a specific impaired waterway with an approved TMDL
  Outlines pathway to meeting water quality standards
  Required to receive §319 grants
WVCA §319 projects include:
  Conservation planning
  Agricultural BMP implementation
  Septic system rehabilitation and pumping
  Stream restoration
Notes: USEPA
WVDEP
WVDEP

## Slide 4: Delisting a Stream
WBP of action complete
Monitoring plan must be approved by WVDEP
  Quality data
  Correct sample locations
One year monitoring plan
  Minimum sample set = 20
  90% of samples must meet WQ standards to delist
Concentration based
  Delisting decisions are concentration based despite TMDL’s being load based
Second Creek, Monroe County, West Virginia.
Kara Grosso

## Slide 5: Combining the §319 Program and Water Quality Monitoring to Delist Streams
Working on a watershed basis
  HUC 10 and 12 levels
  Projects in one watershed may continue over several grants
  Load reductions modeled
Monitoring
  Triggered when load reduction modeling nearly meets WBP goal
    50-75%
  Determine original sample locations
    Pre-TMDL monitoring
    Assessment units
  Pre-TMDL data = pre-project data
  Staff gauge
Staff gauge, Second Creek.
Kara Grosso

## Slide 6: Outcomes
Data provides:
  WVDEP delisting decision
  WBP revision if not delisted
  Instantaneous loading data to compare with modeled TMDL
Funding delineation
  Agency §319 administrative grant covers intense watershed studies
  Watershed based §319 grants cover practice implementation and load reduction modeling
Woodland phlox, Monroe County, West Virginia.
Kara Grosso

## Slide 7: Questions?
Carpenter Creek, Monroe County, West Virginia. Kara Grosso